## Slide 1: Into an automated, cooperative, diverse and integrated futuristic transportation system
Rahul Kala
Motion Planning for Multiple Autonomous Vehicles

## Slide 2: Organized and Unorganized Traffic
A distant future where all vehicles would autonomously be driven would be preceded by a transient period where automated and nonautomated vehicles coexist.
Vanholme, B.; et al. "Highly Automated Driving on Highways Based on Legal Safety," IEEE Transactions on Intelligent Transportation Systems, vol.14, no.1, pp.333-347, March 2013

## Slide 3: Organized and Unorganized Traffic
Organized
Image Courtesy: railway-technical.com, blogs.abc.net.au
Unorganized

## Slide 4: Thesis
Thesis
Trajectory Generation
Intelligent Management of the Transportation System

## Slide 5: Trajectory Generation
A
Static Obstacles
B
C
Select the best plan:
(a) A overtakes B from right, B drifts left, A crosses the obstacles, C waits, (b) A follows B and both cross the obstacles while C waits,
(c) B crosses the obstacles followed by C and A,
(d) C crosses the obstacle a from its left, while A follows B to cross the others
a

## Slide 6: Intelligent Management of the Transportation System
Routing objective/ considerations
Routing frequency
Recurrent or non-recurrent
Traffic Lights
Lane change
Entirely semi-autonomous, mixed, manual
Bookings

## Slide 7: Genetic Algorithm
R1
R2
R3
Overtake seems to be too close, ask R2 to slow
R3 lies directly ahead, ask R3 to drift to its left
GA optimized trajectories
Coordination using traffic heuristics
Under revision: Applied Soft Computing, IF: 2.140

## Slide 8: RRT
Less exploration at the extremes
More exploration at the central areas
In Proc. IEEE Cybernetic Intelligent Systems, Docklands, London, pp. 20-25

## Slide 9: RRT Connect
If prospective collision with a vehicle in the same direction If you cannot overtake, follow – Speed equal to the heading vehicle and re-plan
If prospective collision with a vehicle in the opposite direction: Decrease speed iteratively and re-plan till a feasible plan is reached
If going straight ahead possible, go
Tree expansions
Paladyn Journal of Behavioural Robotics, 2(3): 134-144.

## Slide 10: Multi-Level Planning
Layer 1: Road Selection. Blue=selected road. Red= Road graph
Layer 2: Pathway Selection. Collaboratively decide whether each vehicle goes through left or right of an obstacle. Blue=selected pathway. Red=Entire Pathway Graph
Equal distribution of pathway
Layer 3:Pathway Distribution. At each slice (pathway segment) the expected vehicles at the same time are placed. Red=computed points for the vehicle, Blue=Rough trajectory joining the placement points, Green=Other expected vehicle
Layer 4: Trajectory Generation. Smoothing, collision checking, local optimization
J. Intell. Rob. Syst, DOI:10.1007/s10846-013-9817-7, IF: 0.827

## Slide 11: Dynamic Distributed Lanes
Any general state in graph search
Known trajectory for the state for the higher priority vehicles
Check for all strategies in parallel
Use strategy selection heuristics to prune expansion
Use separation maximization heuristic to place all vehicles in the next state
Modify lanes and trajectories of all vehicles
Overtake Red?, or Follow Red?, or Wait for green to cross obstacle? – try all 3 possibilities

## Slide 12: Fuzzy Logic
Distance from left, right and front boundary/ obstacle
Side: distance of vehicle in wrong side
Angle deviation from road
Turn to avoid obstacle/ overtake vehicle in front
Requested turn: turn to enable another vehicle to overtake
Fuzzy Inference System
Steering
Speed
Inputs
Outputs
Rules
Prototype human designed
Later optimized by Genetic Algorithm
Overtake feasibility assessment
Choose between overtaking and vehicle following
Frame inputs accordingly

## Slide 13: Lateral Potentials
Forward Potential: right/left decided by heuristics/ strategy parameter, time to collision
Side Potential: turn left, inversely proportional to distance
Side Potential: turn right, inversely proportional to distance
Back Potential: right/left decided by heuristics/ strategy parameter, time to collision
Diagonal Potential: turn right, inversely proportional to distance
Diagonal Potential: turn left, inversely proportional to distance
Add potential from all sources, each source indicates whether to steer left or right, and by what magnitude
In Proc. IEEE Intelligent Vehicles Symposium, Alcalá de Henares, Spain, pp. 597-602.

## Slide 14: Elastic Strip
Projected position at the time of arrival
Elastic Strip representing trajectory
Repulsive potentials on strip from vehicles, obstacles, road boundaries
On seeing any new vehicle/ obstacle, try both overtaking from left and right and pick the better plan
Assign highest safe speed as per current position, trim plan such that it is feasible
IEEE Trans. on Intell. Transp. Syst., DOI: 10.1109/TITS.2013.2266355, IF: 3.064

## Slide 15: Logic Based Planning
Behaviours in decreasing order of priority
Obstacle Avoidance
Complete single lane overtake
Centring
Lane Change
Overtake
Single lane overtake
Cancel single lane overtake
Be overtaken
Maintain Separation Steer
Slow Down
Discover Conflicting Interests
Travel Straight
Assess Scenario
Find the highest priority applicable behaviour
Navigate as per the selected behaviour
Cater to in behaviour specifications
Engineering Applications of Artificial Intelligence, 26(5-6): 1588–1601.

## Slide 16: Semi-Autonomous Intelligent Transportation System
Central Information System
Vehicle Route Planning
Vehicle Control
Vehicle Monitoring
Traffic Signal Module
Speed Lane Module
Vehicle Motion Planning
Lane Booking
Road Booking
Scenario Specification
Map/Initial conditions
Traffic at roads
Speed of vehicles at lanes
Position/ Speed
Speed Limit
Booking Specifications
Signal state
Traffic Info.
Lane change, Follow, Stop/Start, Turn
Booked?
Booked?

## Slide 17: Congestion Avoidance in City Traffic
Hypothesis
Make frequent effective short term plans
(Re-)Plan at every crossing
Minimize
(i) Expected travel time
(ii) Expected traffic density
(iii) Expected time to wait at crossings
Plan for a threshold distance from the source
Assume it is possible to reach the goal from the planned state
Like human drivers always see the current traffic and take the best route towards the goal, assuming no dead ends

## Slide 18: Reaching Destination before Deadline with Intelligent Transportation Systems
Road Network Graph
Intelligent Agents Placed at every intersection
Road
Monitor all incoming vehicles. Learn
average speed and variation
Speed assumed for route planning =
Learnt Average Speed - α.Learnt Deviation
More importance of reaching on time = more resistance to risk = earlier start time = high probability of reaching = higher α, and vice versa
High deviation = vehicles in that road vary largely in speed = road is less reliable and should be avoided = larger resistance to risk, and vice versa

## Slide 19: Reaching Destination before Deadline with Cooperative Intelligent Transportation Systems
Cooperative ITS
Cooperative Traffic Lights
Cooperative Lane Changes
Change lights with a preference to the vehicles running late
Change lane to make way for the vehicle running more late
Times in increasing order
Expected Time
Late Time
Cancel Time
Comfortable State
Late State
Very Late State
Give Up State
Vehicle States
Various times at every intersection
Cost of lateness

## Slide 20: Results

## Slide 21: Conclusions
Situational assessment
Context assessment
Algorithm switching
Studying the problems in local settings, using regional data sets
The future is unknown and diverse!

## Slide 22: Thank You
Acknowledgements:
Commonwealth Scholarship Commission in the United Kingdom
British Council